## Slide 1: Processor Datapath

## Slide 2: Introduction
MIPS ISA
  3 Instruction Types
    R-type, I-type, J-type
Datapath and Control Unit
  Simplified
  Pipelined
Simple subset
  Memory reference: lw, sw
  Arithmetic/logical: add, addi, sub, and, or, slt
  Control transfer: beq, j

## Slide 3: Instruction Format Review
Three instruction formats
  R-type
  I-type
  J-type
Fields:
  op: operation of the instruction
  rs, rt, rd: source/destination register specifiers
  shamt: shift amount
  funct: selects variant of the operation in the “op” field
  address/immediate: address offset or immediate value
  target address: target address of the jump instruction
op
target address
0
26
31
6 bits
26 bits
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits

## Slide 4: MIPS Subset
Add, Subtract, AND, OR, SLT
  add rd, rs, rt
  sub rd, rs, rt
  and rd, rs, rt
  or rd, rs, rt
  slt rd, rs, rt
ADD Immediate
  addi rt, rs, imm16
Load, Store
  lw rt, rs, imm16
  sw rt, rs, imm16
BRANCH
  beq rs, rt, imm16
JUMP:
  j target
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
op
target address
0
26
31
6 bits
26 bits

## Slide 5: Instruction Execution
For every instruction:
  Send the program counter (PC) to the memory that contains the code and fetch the instruction from that memory.
  Read one or two registers, using fields of the instruction to select the registers to read. For the load word instruction, we need to read only one register, but most other instructions require that we read two registers.

## Slide 6: Instruction Execution
Fetch:
  Get the next instruction: stored at PC

## Slide 7: Instruction Execution
Decode:
  Opcode determines if the instruction is arithmetic/logical, memory logical, or branch.

## Slide 8: Instruction Execution
  Update PC: PC  target address or PC + 4
  If the instruction is a branch, we have to calculate the target address
  If the instruction is not a branch, the new PC will be PC + 4

## Slide 9: Instruction Execution
  Update PC: PC  target address or PC + 4
  If the instruction is a branch, we have to calculate the target address
  If the instruction is not a branch, the new PC will be PC + 4

## Slide 10: Instruction Execution
Execute:
  Depending on instruction class, we use the ALU to calculate:
    Arithmetic result
    Memory address for load/store
    Branch target address

## Slide 11: Instruction Execution
To read and write registers, we need a register file
  R-types read two registers and write one register
  Memory-reference instructions read one register
    Also access data memory

## Slide 12: Processor Overview
Data “flows” through memory and functional units

## Slide 13: Processor Overview
Can’t just join wires together
  Use multiplexers

## Slide 14: Processor Overview
Multiplexers require selection signals
  Control Signals

## Slide 15: Signals
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses

## Slide 16: Logic Design Review
Combinational Circuits
  Output depends only on current input
  Operate on data
Example: ALU
  Given the same input a combinational circuit will always produce the same output

## Slide 17: Logic Design Review
Sequential Circuits
  Have “state”
  Output depends on current input and previous outputs
Example: Register File
  State elements have at least two inputs: input and clock

## Slide 18: MIPS Register File
32 32-bit registers
One write bus
Two read buses
Selection Inputs
  Write Enable
  Reg. Write
  Reg. Read A
  Reg. Read B

## Slide 19: Write Control Signals
Every Clock Cycle
We do not show a write control signal when a state element is written on every active clock edge.
  Program Counter
When Necessary
If a state element is not updated on every clock, then an explicit write control signal is required.
  Register File

## Slide 20: Datapath Elements
Most elements have 32-bit wide inputs and outputs
Buses labeled with their width

## Slide 21: Datapath Elements - Combinational
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 22: Datapath Elements - Sequential

## Slide 23: Fetch Elements
Memory Unit
Program Counter
Adder

## Slide 24: R-Type Instructions
Read two register operands
Perform arithmetic/logical operation
Write register result

## Slide 25: R-Type Instructions
add $t1, $t2, $t3
RW = 9
RA = 10
RB = 11
ALUctrl = “add”

## Slide 26: Datapath: R-Type Instructions

## Slide 27: I-Type Instructions
Replace one read register, shamt, and funct with 16 bit constant
ALU requires 32-bit inputs
  Sign-extend the 16 bit immediate
    Fill with 0s if the constant is positive
    Fill with 1s if the constant is negative
Choose between the second read registers and the sign extended constant.

## Slide 28: Datapath: I-Type Instructions

## Slide 29: Load/Store Instructions
lw $t1, offset($t2)
sw $t1, offset($t2)
Compute memory address: $t2 + offset
Since offset is 16 bits, it needs to be extended to 32 bits

## Slide 30: Load/Store Instructions
Load: Read memory and update register
Store: Write register value to memory
Elements:
  Register file
  Sign extension unit
  Data memory unit

## Slide 31: Datapath: Load Instruction

## Slide 32: Datapath: Store Instruction

## Slide 33: Branch Instructions
beq $t1, $t2, offset
Read register operands
Compare operands
  Use ALU, subtract and check Zero output
Calculate target address
  Sign-extend displacement
  Shift left 2 places (word displacement)
  Add to PC + 4
    Already calculated by instruction fetch

## Slide 34: Target Address Details
The base for the branch address calculation is the address of the instruction following the branch.
  PC+4
Memory is byte addressed
  The offset field must be shifted left 2 bits

## Slide 35: Branch Instructions
Just re-routes wires
Sign-bit wire replicated

## Slide 36: Branching
beq $t1, $t2, offset
Branch is taken
  When $t1 - $t2 = 0, the zero signal from the ALU
  PC = PC + 4 + 4*offset
Branch is not taken
  PC = PC + 4

## Slide 37: Datapath: Branch

## Slide 38: Jump Instructions
PC = PC[31-28] : Offset << 2

## Slide 39: Single Datapath
All instructions executed in one clock cycle
  Each datapath element can only do one function at a time
  Any element needed more than once must be duplicated
  Hence, we need separate instruction and data memories
Use multiplexers where alternate data sources are used for different instructions

## Slide 40: Datapath

## Slide 41: Control Unit
Take in input
Generate signals for each state element
Generate selection signals for each multiplexor
Generate function signals for ALU
  ALU Control

## Slide 42: ALU Control
MIPS subset: lw, sw, beq, add, addi, sub, and, or, slt
ALU has 4 control inputs
  16 possible functions
ALU Control | Function
0000 | AND
0001 | OR
0010 | Add
0110 | Subtract
0111 | Set-on-less-than
1100 | NOR

## Slide 43: ALU Control
Load/Store: add
Branch: subtract
R-type: depends on funct field
ALU Control | Function
0000 | AND
0001 | OR
0010 | Add
0110 | Subtract
0111 | Set-on-less-than
1100 | NOR

## Slide 44: ALU Control
Opcode determines which type of instruction
The ALUOp is a 2-bit signal derived from this Opcode
ALUOp and the funct field will determine ALU control
Opcode | ALUOp | Operation | Funct | ALU function | ALU Control
Lw | 00 | Load word | XXXXXX | Add | 0010
Sw | 00 | Store word | XXXXXX | Add | 0010
Beq | 01 | Branch | XXXXXX | Subtract | 0110
R-type | 10 | Add | 100000 | Add | 0010
 |  | Subtract | 100010 | Subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | Set-on-Less-Than | 101010 | Set-on-Less-Than | 0111

## Slide 45: ALU Control
Multiple levels of decoding:
  Main Control generates ALUOp
  ALUOp and funct bits determine ALU Control

## Slide 46: ALU Control
  ALUOp and funct bits determine ALU Control
ALUOp1 | ALUOp2 | Funct |  |  |  |  |  | Operation
0 | 0 | X | X | X | X | X | X | 0010 (add)
X | 1 | X | X | X | X | X | X | 0110 (subtract)
1 | X | X | X | 0 | 0 | 0 | 0 | 0010 (add)
1 | X | X | X | 0 | 0 | 1 | 0 | 0110 (subtract)
1 | X | X | X | 0 | 1 | 0 | 0 | 0000 (and)
1 | X | X | X | 0 | 1 | 0 | 1 | 0001 (or)
1 | X | X | X | 1 | 0 | 1 | 0 | 0111 (slt)

## Slide 47: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 48: Main Control Unit
Observations
  The opcode is always contained in bits 31:26. We will refer to this field as Op[5:0].
  The two registers to be read are always specified by the rs and rt fields, at positions 25:21 and 20:16. This is true for the R-type instructions, branch equal, and for store.
  The base register for load and store instructions is always in bit positions 25:21 (rs).
  The 16-bit offset for branch equal, load, and store is always in positions 15:0.
  The destination register is in one of two places.
    For a load it is in bit positions 20:16 (rt)
    For an R-type instruction it is in bit positions 15:11 (rd)
      We will need to add a multiplexor to select which field of the instruction is used to indicate the register number to be written.

## Slide 49: Datapath with ALU Control

## Slide 50: Control Signals – Register Destination
RegDst
  Deasserted: the register destination number for the write register comes the rt field (bits 20:16)
  Asserted: the register destination number for the write register comes the rd field (bits 15:11)

## Slide 51: Control Signals – Register Write
RegWrite
  Asserted: the register destination on the write register input is written with the value on the write data input

## Slide 52: Control Signals – ALU Source
ALUSrc
  Deasserted: The second ALU operand comes from the second register file output
  Asserted: The second ALU operand is the sign-extended lower 16 bits of the instruction

## Slide 53: Control Signals - PCSrc
Program Counter Source
  Deasserted: The PC is replaced by PC + 4
  Asserted: The PC is replaced by a branch target address

## Slide 54: Control Signals – Memory Read
MemRead
  Asserted: Data memory contents designated by the address input are put on the read data output.

## Slide 55: Control Signals – Memory Write
MemWrite
  Asserted: Data memory contents designated by the address input are replaced by the value on the write data input.

## Slide 56: Control Signals – Memory to Register
MemtoReg
  Deasserted: The value fed to the register write data input comes from the ALU
  Asserted: The value fed to the register write data input comes from the data memory.

## Slide 57: Control Signals
All but one signal can be set based only on the opcode
PCSrc is the exception
  Relies on the result of a branch
  PCSrc should be set if the instruction is beq and the zero output of the ALU is asserted

## Slide 58: Datapath With Control

## Slide 59: Opcode to Control
Instruction | RegDst | ALUSrc | MemtoReg | RegWrite
R-Format | 1 | 0 | 0 | 1
Lw | 0 | 1 | 1 | 1
Sw | X | 1 | X | 0
Beq | X | 0 | X | 0
Instruction | MemRead | MemWrite | Branch | ALUOp1 | ALUOp0
R-Format | 0 | 0 | 0 | 1 | 0
Lw | 1 | 0 | 0 | 0 | 0
Sw | 0 | 1 | 0 | 0 | 0
Beq | 0 | 0 | 1 | 0 | 1

## Slide 60: R-Type Instruction

## Slide 61: Load Instruction

## Slide 62: Branch-on-Equal Instruction

## Slide 63: Opcode to Control
In/Out | Signal | R-Format | Lw | Sw | Beq
Inputs | Op5 | 0 | 1 | 1 | 0
 | Op4 | 0 | 0 | 0 | 0
 | Op3 | 0 | 0 | 1 | 0
 | Op2 | 0 | 0 | 0 | 1
 | Op1 | 0 | 1 | 1 | 0
 | Op0 | 0 | 1 | 1 | 0
Outputs | RegDst | 1 | 0 | X | X
 | ALUSrc | 0 | 1 | 1 | 0
 | MemToReg | 0 | 1 | X | X
 | RegWrite | 1 | 1 | 0 | 0
 | MemRead | 0 | 1 | 0 | 0
 | MemWrite | 0 | 0 | 1 | 0
 | Branch | 0 | 0 | 0 | 1
 | ALUOp1 | 1 | 0 | 0 | 0
 | ALUOp0 | 0 | 0 | 0 | 1

## Slide 64: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
  00
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 65: Datapath With Jumps Added

## Slide 66: Single-Cycle Implementation
Every instruction begins execution on one clock edge and completes execution on the next clock edge.
Clock cycle time must be at least as long as the longest instruction (load word).
    Cycle time =
      PC’s propagation time +
      Instruction Memory Access Time +
      Register File Access Time +
      ALU Delay (address calculation) +
      Data Memory Access Time +
      Register File Setup Time +
      Clock Skew

## Slide 67: Single-Cycle Implementation
Every instruction begins execution on one clock edge and completes execution on the next clock edge.
Clock cycle time must be at least as long as the longest instruction (load word).
    The cycle time for load is much longer than any other instruction

## Slide 68: Single-Cycle Implementation
Single-Cycle implementation is not practical
  Unable to implement more complex instructions
  Cannot make improves that will speed up the system unless those improvements are to load
  Violates the design principle of making the common case fast
  Some functional units must be duplicated, increasing hardware cost

## Slide 69: Pipelining
Pipelining is an implementation technique in which multiple instructions are overlapped in execution.
  Pipelining is nearly universal.

## Slide 70: Analogy for Pipelining: Laundry
Nonpipelined approach:
  Place one dirty load of clothes in the washer.
  When the washer is finished, place the wet load in the dryer.
  When the dryer is finished, place the dry load on a table and fold.
  When folding is finished, put the clothes away.
When the clothes are put away, the next load can begin.

## Slide 71: Analogy for Pipelining: Laundry
Pipelined approach:
    Place one dirty load (load A) of clothes in the washer.
    When the washer is finished, place load A in the dryer and start a new load (load B) in the washer.
    When the dryer is finished, place load A on the table to fold, place load B in the dryer, and start a new load (load C) in the washer.
    When folding is finished, put away load A, fold load B, place load C in the dryer, start load D in the washer.

## Slide 72: Analogy for Pipelining: Laundry

## Slide 73: Pipelining Paradox
One load of laundry still takes the same amount of time.
The amount of time it takes to do many loads of laundry is shorter with pipelining.
Pipelining improves throughput.

## Slide 74: Pipelining Speedup
If all the stages take about the same amount of time and there is enough work to do, then the speedup due to pipelining is roughly equal to the number of stages in the pipeline.
Laundry Analogy:
4 stages (washing, drying, folding, putting away)
  20 loads pipelined would take about 5 times as long as 1 load
  20 loads of sequential laundry takes 20 times as long as 1 load

## Slide 75: MIPS Pipeline
Fetch instruction from memory.
Read registers while decoding the instruction.
Execute the operation or calculate an address.
Access an operand in data memory.
Write the result into a register.
Instruction Fetch (IF)
Instruction Decode (ID)
Execution (EX)
Memory Access (MEM)
Write Back (WB)

## Slide 76: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
  Programs execute billions of instructions – throughput is important!

## Slide 77: Pipelining and ISA Design
MIPS ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 78: MIPS Pipelined Datapath
WB
Branch

## Slide 79: Pipelined Execution

## Slide 80: Pipeline registers
Need registers between stages
  To hold information produced in previous cycle

## Slide 81: IF for Load

## Slide 82: ID for Load

## Slide 83: EX for Load

## Slide 84: MEM for Load

## Slide 85: WB for Load
Wrong register number

## Slide 86: Corrected Datapath for Load

## Slide 87: Pipelined Control

## Slide 88: Pipelined Control
Instruction fetch:
  PC written on every clock cycle
  Instruction memory read on every clock cycle
  no optional control lines
Instruction decode/register file read
  Register file read on every clock cycle
  no optional control lines
Execution:
  Set RegDst: select the Result register
  Set ALUOp: select the ALU operation
  Set ALUSrc. select either Read data 2 or a sign-extended immediate for the ALU.
Memory access:
  Set Branch: affects PCSrc
  Set MemRead
  Set MemWrite.
Write back:
  Set MemtoReg: decides between sending the ALU result or the memory value to the register file
  Set Reg-Write: specifies whether the register file can be written

## Slide 89: Pipelined Control
RegDst
ALUSrc
ALUOp1
ALUOp0
Branch
MemRead
MemWrite
MemtoReg
Regwrite

## Slide 90: Pipelined Control

## Slide 91: Hazards
Situations that prevent starting the next instruction in the next cycle
Structure hazard
  A required resource is busy
Data hazard
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Deciding on control action depends on previous instruction

## Slide 92: Structure Hazards
Conflict for use of a resource
In MIPS pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 93: Data Hazards
An instruction depends on completion of data access by a previous instruction
  add $s0, $t0, $t1
  sub $t2, $s0, $t3

## Slide 94: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 95: Forwarding
Forwarding: the result is passed forward from an earlier instruction to a later instruction.

## Slide 96: Load-Use Data Hazard
Can’t always avoid stalls by forwarding

## Slide 97: Pipeline Stalls
A stall (bubble) is implemented with a nop
  “No operation”
Force control values in ID/EX register to 0

## Slide 98: Stall/Bubble in the Pipeline
Stall inserted here

## Slide 99: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
stall
stall
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
11 cycles
13 cycles

## Slide 100: Control Hazards
Branch Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch

## Slide 101: Stall on Branch
Wait until branch outcome determined before fetching next instruction

## Slide 102: Branch Prediction
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In MIPS pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 103: Predict Branch Not Taken
If branch is determined as taken in MEM:
PC
Flush these instructions
(Set control values to 0)

## Slide 104: Predict Branch Not Taken
Prediction correct
Prediction incorrect

## Slide 105: Predict Branch Not Taken
If branches are untaken half the time, and if it costs little to discard the instructions, this optimization halves the cost of control hazards.

## Slide 106: Branch Prediction
Static branch prediction
  Based on typical branch behavior
  Example: loop and if-statement branches
    Predict backward branches taken
    Predict forward branches not taken

## Slide 107: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction
  Branch History Table
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 108: 1-Bit Predictor: Shortcoming
Inner loop branches mispredicted twice!
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer
  Mispredict as taken on last iteration of inner loop
  Then mispredict as not taken on first iteration of inner loop next time around

## Slide 109: 2-Bit Predictor
Only change prediction on two successive mispredictions

## Slide 110: Delayed Decision
Branch Instruction
Execute the next sequential instruction
Execute the instruction that resulted from the branch
add $4, $5, $6 -> beq $1, $2, 40
beq $1, $2, 40 -> add $4, $5, $6
<branch result> <branch result>

## Slide 111: Cycle Time Matters
Delayed branches work when branches are short
  no processor uses a delayed branch of more than 1 cycle
Longer branch delays rely on hardware based branch prediction

## Slide 112: Reducing Branch Delay
Insight:
  many branches rely only on simple tests
    can be implemented with a few gates over an ALU
  more complex branches take two instructions
    slt followed by beq/bne
Move hardware to determine outcome to ID stage
  Target address adder
  Register comparator
Reduces the penalty of a branch to only one instruction if the branch is taken

## Slide 113: Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation

## Slide 114: Exceptions and Interrupts
“Unexpected” events requiring change in flow of control
Exception
  Arises within the CPU
  Examples: undefined opcode, overflow, syscall
Interrupt
  From an external I/O controller

## Slide 115: Handling Exceptions
In MIPS, exceptions managed by a System Control Coprocessor (CP0)
Save PC of offending (or interrupted) instruction
  In MIPS: Exception Program Counter (EPC)
Save indication of the problem
  In MIPS: Status register
    0000 – undefined instruction
    0180 – arithmetic overflow
Jump to handler

## Slide 116: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use EPC to return to program
Otherwise
  Terminate program
  Report error using EPC

## Slide 117: Exceptions in a Pipeline
Another form of control hazard
Consider overflow on add in EX stage
  add $1, $2, $1
  Prevent $1 from being overwritten
  Complete previous instructions
  Flush add and subsequent instructions
  Set Cause and EPC register values
  Transfer control to handler
Similar to mispredicted branch
  Use much of the same hardware

## Slide 118: Multiple Exceptions
Pipelining overlaps multiple instructions
  Could have multiple exceptions at once
Simple approach: deal with exception from earliest instruction
  Flush subsequent instructions

## Slide 119: Fallacies
Pipelining is easy
  The basic idea is easy
  The devil is in the details
    e.g., detecting data hazards
Pipelining is independent of technology
  So why haven’t we always done pipelining?
  More transistors make more advanced techniques feasible
  Pipeline-related ISA design needs to take account of technology trends

## Slide 120: Pitfalls
Poor ISA design can make pipelining harder
  e.g., complex instruction sets (VAX, IA-32)
    Significant overhead to make pipelining work
  e.g., complex addressing modes
    Register update side effects, memory indirection
  e.g., delayed branches
    Advanced pipelines have long delay slots

## Slide 121: Concluding Remarks
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Exceptions are handled by a outside handler and control hazard logic.